## Slide 1: GROUP WORK ASSIGNMENT FOR INTRODUCTION TO COMPUTER NETWORKS COURSE UNIT: IST 11O4 SEMESTER:1 LECTURER: MALE VINCENT 2026 YEAR: 1 BY GROUP 1
NAME | REGESTRATION NO. | STUDENT NO:
AINEBYONA VICTOR | 26/U/04227/PSA | 2600703692
ACHUDA FREDRICK | 26/U/29544/PSA | 2600729544
AKAMPURIRA IAN | 26/U/03698/PS | 2600703698
ODOI VINCENT | 26/U/30208/PS | 2600730208
ABOKU GEORGE PHILIP | 26/U/03678/PSA | 2600703678
WAMANGA SHAMIHA | 26/U/04227/PS | 2600704227

## Slide 2: NETWORK MODELS
They are basically two network models
OSI model
TCP/IP model

## Slide 3: OSI(OPEN SYSTEM INTERCONNECTION) MODEL
This was based on the propsal by the ISO( international Standards Organisation.) (19 )
Then revised in 1995 from ISO to OSI model because it deals with connecting open systems that is to say the systems are open for communication with other systems.
The model has seven layers.
The OSI model also tell what each layer should do.

## Slide 4: PRINCIPLES THAT WERE APPLIED TO ARRIVE TO THE SEVEN LAYERS
A layer should be created where a different abstraction(simplification) is needed.
Each layer should perfom a well defined function.
The function of each layer should be chosen with an eye to ward defining internationally standardised protocols.
The boundaries should minimise the information flow across the interfaces
The number of layers should be large enough that distinct functions need not to be thrown together but small enough that the architecture does not become too big.

## Slide 5: Physical Layer
This is the first and oldest layer of the OSI model.
Its responsible for converting and transmitting raw binary data bits(0s and1s) across a physical network medium.
Sends individial raw data bits from one node to another with out interpreting their meanig.
It also converts digital bits into electrical voltages, light pulses or radio frequency waves.
manages the transmission speed (bit rate) and clock synchronization between the sender an reciever.
controls how data flows across the medium using simplex, half-duplex and full duplex.
Also defines how physical devices are arranged, such as in star ,bus, and many others
The standard protocols are governed by specifications in the Cable standards(Ethernet), wireless standards(wifi , bluetooth), and fiber optic standards.

## Slide 6: Data Link Layer
It is the layer 2 in the OSI model.
Is responsible for node to node data delivery and error free transfer between directly connected devices on the same local network.
Can move ecapsulates packets( frames) from one adjacent computer to another, cannot move frames across routers
Requires MAC address or physical address
Detects and corrects transimission errors using techniques like Cyclic Redundancy check(CRC) in Frame Check Sequence(FCS)
Protocols defined include Ethernet Protocol and Point-to-Point Protocol (PPP)
Device example: Switch

## Slide 7: SUB LAYERS OF DATA LINK LAYER
These include; Logical Link Control (LLC) and the Media Access Control (MAC)
Logical Link Control (LLC)
Data Link layer addressing, flow control, address notification, error control
Media Access Control (MAC)
Determines which computer has access to the network media at any given time
Determines where one frame ends and the next one starts, called frame synchronization

## Slide 8: Network Layer
Responsible for moving packets (data) from one end of the network to the other, called end-to-end communications
Requires logical addresses such as IP addresses
Device example: Router
Routing is the ability of various network devices and their related software to move data packets from source to destination

## Slide 9: Transport Layer
Takes data from higher levels of OSI Model and breaks it into segments that can be sent to lower-level layers for data transmission
Conversely, reassembles data segments into data that higher-level protocols and applications can use
 Also puts segments in correct order (called sequencing ) so they can be reassembled in correct order at destination
Concerned with the reliability of the transport of sent data
May use a connection-oriented protocol such as TCP to ensure destination received segments
May use a connectionless protocol such as UDP to send segments without assurance of delivery
Uses port addressing

## Slide 10: Session Layer
Responsible for managing the dialog between networked devices
Establishes, manages, and terminates connections
Provides duplex, half-duplex, or simplex communications between devices
Provides procedures for establishing checkpoints, adjournment, termination, and restart or recovery procedures

## Slide 11: Presentation Layer
This is concerned with how data is presented to the network
This handles three primary tasks:
Translation; this changes data so that another computer can understand it
Compression; this makes data smaller to send more data in the same amount of time
Encryption; Encodes data to protect from interception or eavesdropping.

## Slide 12: Application Layer
Contains all services or protocols needed by application software or operating system to communicate on the network.
Examples
Firefox web browser uses HTTP (Hyper-Text Transport Protocol)
E-mail program may use POP3 (Post Office Protocol version 3) to read e-mails and SMTP (Simple Mail Transport Protocol) to send e-mails

## Slide 13: TRANSMISSION CONTROL PROTOCOL/INTERNET PROTOCOL
TCP/IP

## Slide 14: TCP/IP
Consists of 4 major layers
Network layer
Internent layer
Transport layer
Application layer

## Slide 15: NETWORK LAYER
Responsible for transmiting data over the physical network
Hardles hardware addressing and error detection.
Combines the functions of the phyiscal and data link layer of the OSI model.
PROTOCOLS;Ethernet: connects devices via physical media.
WiFi: connects devices via wireless media.

## Slide 16: INTERNET LAYER
Responsible for logical adressing and routing of pockets between networks.
Determines the best path for data transmission
Protocals:IP(IPV4/IPV6) Aids in locating the devices via internet.

## Slide 17: TRANSPORT LAYER
Provides end to end communications between devices.
Ensures reliable and fast data delivery
Performs segmentation flow controls and error recovery
Protocols; TCP ensures reliable conection oriented
UDP ensures faster connections.

## Slide 18: APPLICATION LAYER
Provides network services directely to user applications
Allows users to access network resources
Protocols :HTTP, HTTPs DNS

## Slide 19: SIMILARITIES 0SI AND TCP/IP
Both use layers to organise network communication
Both have Application, Transport and Network communication
Both describe how data move from one.
Both help with network design , trouble shooting and understand protocols.
The transport layer in both models provides end to end communication.

## Slide 20: DIFFERENCES BETWEEN OSI AND TCP/IP
OSI | TCP/IP
Has 7 layers | Has 4 layers
Separates application pressentation annd session | Combines them into the application layer.
Separates physical and data link | Combines them into Network.
Primarily a conceptual model | Protocol architecture used by the internet
Designed as a general network refference frame work. | envolved from the protocols used to build interconnected networks.